## Slide 1: EDGES, CORNERS, AND BLOBS

## Slide 2: EDGE DETECTION
Slides from Svetlana Lazebnik

## Slide 3: Edge Detection
Winter in Kraków photographed by Marcin Ryczek

## Slide 4: Edge Detection
Goal: Identify sudden changes (discontinuities) in an image
  Intuitively, most semantic and shape information from the image can be encoded in the edges
  More compact than pixels
Ideal: artist’s line drawing (but artist is also using object-level knowledge)
Source: D. Lowe

## Slide 5: Origin of Edges
Edges are caused by a variety of factors:
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity
Source: Steve Seitz

## Slide 6: Review: Linear Filtering
Image blurring
Separability
Median filtering

## Slide 7: Edge Detection
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative

## Slide 8: Derivatives with Convolution
For 2D function f(x,y), the partial derivative is:
For discrete data, we can approximate using finite differences:
To implement the above as convolution, what would be the associated filter?
Source: K. Grauman

## Slide 9: Partial Derivatives of an Image
Which shows changes with respect to x?
-1 1
1 -1
or
-1 1

## Slide 10: Finite Difference Filters
Other approximations of derivative filters
-1 | -1 | -1
0 | 0 | 0
1 | 1 | 1
-1 | 0 | 1
-1 | 0 | 1
-1 | 0 | 1
Prewitt
=
=
-1 | -2 | -1
0 | 0 | 0
1 | 2 | 1
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
Sobel
=
=

## Slide 11: Image Gradient
The gradient points in the direction of most rapid increase in intensity
The gradient of an image:
The gradient direction is given by
Source: Steve Seitz
The edge strength is given by the gradient magnitude
How does this direction relate to the direction of the edge?

## Slide 12: Application: Gradient-Domain Image Editing
Goal: solve for pixel values in the target region to match gradients of the source region while keeping background pixels the same
P. Perez, M. Gangnet, A. Blake, Poisson Image Editing, SIGGRAPH 2003

## Slide 13: Effects of Noise
Consider a single row or column of the image
Where is the edge?
Source: S. Seitz
Notes: How to fix?

## Slide 14: Solution: Smooth First
To find edges, look for peaks in
f
g
f * g
Source: S. Seitz

## Slide 15: Derivative Theorem of Convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz

## Slide 16: Derivative of Gaussian Filters
Which one finds horizontal/vertical edges?
x-direction
y-direction

## Slide 17: Derivative of Gaussian Filters
Are these filters separable?
x-direction
y-direction

## Slide 18: Recall: Separability of the Gaussian Filter
Source: D. Lowe

## Slide 19: Scale of Gaussian Derivative Filter
Smoothed derivative removes noise, but blurs edge. Also finds edges at different “scales”
1 pixel
3 pixels
7 pixels
Source: D. Forsyth

## Slide 20: Review: Smoothing vs. Derivative Filters
Smoothing filters
  Gaussian: remove “high-frequency” components; “low-pass” filter
  Can the values of a smoothing filter be negative?
  What should the values sum to?
    One: constant regions are not affected by the filter
Derivative filters
  Derivatives of Gaussian
  Can the values of a derivative filter be negative?
  What should the values sum to?
    Zero: no response in constant regions
  High absolute value at points of high contrast

## Slide 21: The Canny Edge Detector
Filter image with derivative of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression:
  Thin wide “ridges” down to single pixel width
Linking and thresholding (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.

## Slide 22: The Canny Edge Detector
original image
Slide credit: Steve Seitz

## Slide 23: The Canny Edge Detector
norm of the gradient

## Slide 24: The Canny Edge Detector
thresholding

## Slide 25: The Canny Edge Detector
thresholding
How to turn these thick regions of the gradient into curves?

## Slide 26: Non-Maximum Suppression
Check if pixel is local maximum along gradient direction, select single max across width of the edge
  requires checking interpolated pixels p and r

## Slide 27: The Canny Edge Detector
thinning
(non-maximum suppression)
Problem: pixels along this edge didn’t survive the thresholding

## Slide 28: Hysteresis Thresholding
Use a high threshold to start edge curves, and a low threshold to continue them.
Source: Steve Seitz

## Slide 29: Hysteresis Thresholding
original image
high threshold
(strong edges)
low threshold
(weak edges)
hysteresis threshold
Source: L. Fei-Fei

## Slide 30: Recap: Canny Edge Detector
Compute x and y gradient images
Find magnitude and orientation of gradient
Non-maximum suppression:
  Thin wide “ridges” down to single pixel width
Linking and thresholding (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.

## Slide 31: Image Gradients vs. Meaningful Contours
Berkeley segmentation database: http://www.eecs.berkeley.edu/Research/Projects/CS/vision/grouping/segbench/
image
human segmentation
gradient magnitude

## Slide 32: Data-Driven Edge Detection
P. Dollar and L. Zitnick, Structured forests for fast edge detection, ICCV 2013
Training data
Input images
Ground truth
Output

## Slide 33: CORNERS
Slides are from Svetlana Lzebnik

## Slide 34: Feature Extraction: Corners
9300 Harris Corners Pkwy, Charlotte, NC

## Slide 35: Why Extract Features?
Motivation: panorama stitching
  We have two images – how do we combine them?

## Slide 36: Why Extract Features?
Motivation: panorama stitching
  We have two images – how do we combine them?
Step 1: extract features
Step 2: match features

## Slide 37: Why Extract Features?
Motivation: panorama stitching
  We have two images – how do we combine them?
Step 1: extract features
Step 2: match features
Step 3: align images

## Slide 38: Characteristics of Good Features
Repeatability
  The same feature can be found in several images despite geometric and photometric transformations
Saliency
  Each feature is distinctive
Compactness and efficiency
  Many fewer features than image pixels
Locality
  A feature occupies a relatively small area of the image; robust to clutter and occlusion

## Slide 39: Applications
Feature points are used for:
  Image alignment
  3D reconstruction
  Motion tracking
  Robot navigation
  Indexing and database retrieval
  Object recognition

## Slide 40: A Hard Feature Matching Problem
NASA Mars Rover images

## Slide 41: Answer Below (look for tiny colored squares…)
NASA Mars Rover images
with SIFT feature matches Figure by Noah Snavely

## Slide 42: Corner Detection: Basic Idea
We should easily recognize the point by looking through a small window
Shifting a window in any direction should give a large change in intensity
“edge”: no change along the edge direction
“corner”: significant change in all directions
“flat” region: no change in all directions

## Slide 43: Corner Detection: Mathematics
Change in appearance of window W for the shift [u,v]:
I(x, y)
E(u, v)
E(3,2)

## Slide 44: Corner Detection: Mathematics
I(x, y)
E(u, v)
E(0,0)
Change in appearance of window W for the shift [u,v]:

## Slide 45: Corner Detection: Mathematics
We want to find out how this function behaves for small shifts
E(u, v)
Change in appearance of window W for the shift [u,v]:
Notes: Specifically, E has to have a unique minimum at (0,0)

## Slide 46: Corner Detection: Mathematics
First-order Taylor approximation for small motions [u, v]:
Let’s plug this into E(u,v):

## Slide 47: Corner Detection: Mathematics
The quadratic approximation can be written as
where M is a second moment matrix computed from image derivatives:
(the sums are over all the pixels in the window W)

## Slide 48: Interpreting the Second Moment Matrix
The surface E(u,v) is locally approximated by a quadratic form. Let’s try to understand its shape.
  Specifically, in which directions does it have the smallest/greatest change?
E(u, v)

## Slide 49: Interpreting the Second Moment Matrix
First, consider the axis-aligned case (gradients are either horizontal or vertical)
If either a or b is close to 0, then this is not a corner, so look for locations where both are large.

## Slide 50: Interpreting the Second Moment Matrix
Consider a horizontal “slice” of E(u, v):
This is the equation of an ellipse.

## Slide 51: Interpreting the Second Moment Matrix
Consider a horizontal “slice” of E(u, v):
This is the equation of an ellipse.
The axis lengths of the ellipse are determined by the eigenvalues and the orientation is determined by R
direction of the slowest change
direction of the fastest change
(max)-1/2
(min)-1/2
Diagonalization of M:

## Slide 52: Visualization of Second Moment Matrices

## Slide 53: Visualization of Second Moment Matrices

## Slide 54: Interpreting the Eigenvalues
1
2
“Corner” 1 and 2 are large, 1 ~ 2; E increases in all directions
1 and 2 are small; E is almost constant in all directions
“Edge” 1 >> 2
“Edge” 2 >> 1
“Flat” region
Classification of image points using eigenvalues of M:

## Slide 55: Corner Response Function
“Corner” R > 0
“Edge” R < 0
“Edge” R < 0
“Flat” region
|R| small
α: constant (0.04 to 0.06)

## Slide 56: The Harris Corner Detector
Compute partial derivatives at each pixel
Compute second moment matrix M in a Gaussian window around each pixel:
C.Harris and M.Stephens. “A Combined Corner and Edge Detector.” Proceedings of the 4th Alvey Vision Conference: pages 147—151, 1988.

## Slide 57: The Harris Corner Detector
Compute partial derivatives at each pixel
Compute second moment matrix M in a Gaussian window around each pixel
Compute corner response function R
C.Harris and M.Stephens. “A Combined Corner and Edge Detector.” Proceedings of the 4th Alvey Vision Conference: pages 147—151, 1988.

## Slide 58: Harris Detector: Steps

## Slide 59: Harris Detector: Steps
Compute corner response R

## Slide 60: The Harris Corner Detector
Compute partial derivatives at each pixel
Compute second moment matrix M in a Gaussian window around each pixel
Compute corner response function R
Threshold R
Find local maxima of response function (nonmaximum suppression)
C.Harris and M.Stephens. “A Combined Corner and Edge Detector.” Proceedings of the 4th Alvey Vision Conference: pages 147—151, 1988.

## Slide 61: Harris Detector: Steps
Find points with large corner response: R > threshold

## Slide 62: Harris Detector: Steps
Take only the points of local maxima of R

## Slide 63: Harris Detector: Steps

## Slide 64: Invariance and Covariance
We want corner locations to be invariant to photometric transformations and covariant to geometric transformations
  Invariance: image is transformed and corner locations do not change
  Covariance: if we have two transformed versions of the same image, features should be detected in corresponding locations

## Slide 65: Activity
Discuss in pairs and decide:
I may randomly ask a pair to respond.
Is Harris corner detection invariant to
Affine intensity changes
Image translation
Image rotation
Image scaling
I  a I + b

## Slide 66: Affine Intensity Change
Only derivatives are used => invariance to intensity shift I  I + b
Intensity scaling: I  a I
R
x (image coordinate)
threshold
R
x (image coordinate)
Partially invariant to affine intensity change
I  a I + b

## Slide 67: Image Translation
Derivatives and window function are shift-invariant
Corner location is covariant w.r.t. translation

## Slide 68: Image Rotation
Second moment ellipse rotates but its shape (i.e. eigenvalues) remains the same
Corner location is covariant w.r.t. rotation

## Slide 69: Scaling
All points will be classified as edges
Corner
Corner location is not covariant to scaling!

## Slide 70: BLOB DETECTION
Slides from Svetlana Lazebnik

## Slide 71: Blob Detection

## Slide 72: Feature Detection with Scale Selection
We want to extract features with characteristic scale that is covariant with the image transformation

## Slide 73: Blob Detection: Basic idea
To detect blobs, convolve the image with a “blob filter” at multiple scales and look for extrema of filter response in the resulting scale space.

## Slide 74: Blob Detection: Basic Idea
Find maxima and minima of blob filter response in space and scale
*
=
maxima
minima
Source: N. Snavely

## Slide 75: Blob Filter
Laplacian of Gaussian: Circularly symmetric operator for blob detection in 2D

## Slide 76: Recall: Edge Detection
f
Source: S. Seitz
Edge
Derivative of Gaussian
Edge = maximum of derivative

## Slide 77: Edge Detection, Take 2
f
Edge
Second derivative of Gaussian (Laplacian)
Edge = zero crossing of second derivative
Source: S. Seitz
Notes: An edge filtered with the Laplacian of Gaussian is the difference between the blurry edge and the original edge.

## Slide 78: From Edges to Blobs
Edge = ripple
Blob = superposition of two ripples
Spatial selection: the magnitude of the Laplacian response will achieve a maximum at the center of the blob, provided the scale of the Laplacian is “matched” to the scale of the blob
maximum

## Slide 79: Scale Selection
We want to find the characteristic scale of the blob by convolving it with Laplacians at several scales and looking for the maximum response
However, Laplacian response decays as scale increases:
increasing σ
original signal (radius=8)

## Slide 80: Scale Normalization
The response of a derivative of Gaussian filter to a perfect step edge decreases as σ increases
Notes: The area under the first derivative of Gaussian from –infinity to 0 is equal to the value of the Gaussian at zero

## Slide 81: Scale Normalization
The response of a derivative of Gaussian filter to a perfect step edge decreases as σ increases
To keep response the same (scale-invariant), must multiply Gaussian derivative by σ
Laplacian is the second Gaussian derivative, so it must be multiplied by σ2

## Slide 82: Effect of Scale Normalization
Scale-normalized Laplacian response
Unnormalized Laplacian response
Original signal
maximum

## Slide 83: Blob Detection in 2D
Laplacian of Gaussian: Circularly symmetric operator for blob detection in 2D
Scale-normalized:

## Slide 84: Scale Selection
At what scale does the Laplacian achieve a maximum response to a binary circle of radius r?
r
image
Laplacian

## Slide 85: Scale Selection
At what scale does the Laplacian achieve a maximum response to a binary circle of radius r?
To get maximum response, the zeros of the Laplacian have to be aligned with the circle
The Laplacian is given by (up to scale):
Therefore, the maximum response occurs at
r
image
circle
Laplacian
0

## Slide 87: Characteristic Scale
We define the characteristic scale of a blob as the scale that produces peak of Laplacian response in the blob center
characteristic scale
T. Lindeberg (1998). "Feature detection with automatic scale selection." International Journal of Computer Vision 30 (2): pp 77--116.

## Slide 88: Scale-Space Blob Detector
Convolve image with scale-normalized Laplacian at several scales

## Slide 89: Scale-Space Blob Detector: Example

## Slide 90: Scale-Space Blob Detector: Example

## Slide 91: Scale-Space Blob Detector
Convolve image with scale-normalized Laplacian at several scales
Find maxima of squared Laplacian response in scale-space

## Slide 92: Scale-Space Blob Detector: Example

## Slide 93: Efficient Implementation
Approximating the Laplacian with a difference of Gaussians:
(Laplacian)
(Difference of Gaussians)

## Slide 94: Efficient Implementation
David G. Lowe. "Distinctive image features from scale-invariant keypoints.” IJCV 60 (2), pp. 91-110, 2004.

## Slide 95: From Feature Detection to Feature Description
Scaled and rotated versions of the same neighborhood will give rise to blobs that are related by the same transformation
What to do if we want to compare the appearance of these image regions?
  Normalization: transform these regions into same-size circles
  Problem: rotational ambiguity

## Slide 96: Eliminating Rotation Ambiguity
To assign a unique orientation to circular image windows:
  Create histogram of local gradient directions in the patch
  Assign canonical orientation at peak of smoothed histogram
0
2
p

## Slide 97: SIFT Features
Detected features with characteristic scales and orientations:
David G. Lowe. "Distinctive image features from scale-invariant keypoints.” IJCV 60 (2), pp. 91-110, 2004.

## Slide 98: From Feature Detection to Feature Description
Detection is covariant:
  features(transform(image)) = transform(features(image))
Description is invariant:
  features(transform(image)) = features(image)

## Slide 99: SIFT Descriptors
David G. Lowe. "Distinctive image features from scale-invariant keypoints.” IJCV 60 (2), pp. 91-110, 2004.

## Slide 100: Properties of SIFT
Extraordinarily robust detection and description technique
  Can handle changes in viewpoint
    Up to about 60 degree out-of-plane rotation
  Can handle significant changes in illumination
    Sometimes even day vs. night
  Fast and efficient—can run in real time
  Lots of code available
Source: N. Snavely

## Slide 101: Affine adaptation
Affine transformation approximates viewpoint changes for roughly planar objects and roughly orthographic cameras

## Slide 102: Affine Adaptation
direction of the slowest change
direction of the fastest change
(max)-1/2
(min)-1/2
Consider the second moment matrix of the window containing the blob:
Recall:
This ellipse visualizes the “characteristic shape” of the window

## Slide 103: Affine Adaptation Example
Scale-invariant regions (blobs)

## Slide 104: Affine Adaptation Example
Affine-adapted blobs